## Slide 1: Hyperlynx SI modeling overview Dmitry Vasilchenko
Where today meets tomorrow.
Restricted © Siemens 2022

## Slide 2: BoardSim SI modeling
Trace Modeler builds crossections, accounts for area fills, finds coupled nets
Via Modeler runs for vias/pins
IBIS models for devices

## Slide 3: SI modeling: 2D vs 3D models

## Slide 4: SI modeling components, BoardSim
Trace Modeler
  Builds nGrpah with connected transmission lines and via/pin ports; finds aggressors
Field Solver
  Solves crossections for RLCG matrixes
Via Modeler
  Lumped via model as LC chain (default)
  Advanced via model as spice model
  BoardSim does not directly support 3D via model, only via in 3D areas
3D Area manager
  Replaces insides of 3D area with a spice model from solved in HLAS
Model Builder
  Loads IBIS, EBD and EMD models, finds switching coefficients k(t) for IBIS drivers
Netlister
  Makes binary netlist basing on nGraph, Via Model, Model builder, hybrid s-parameter model.
SimAPI
  Runs simulator of choice (HyperSim, ADMS, HSPICE) for a given binary netlist
EZWave
  WDB Server stores and handles waveforms for all time domain simulations

## Slide 5: LineSim SI simulation
Field Solver
  Solves t-lines for RLCG matrixes (coupled, AF)
Via Modeler
  Lumped LC model (default)
  Advanced via model
  3D via model - native support
Model Builder
  Loads IBIS, EBD and EMD models, finds switching coefficients k(t) for IBIS drivers
FFS Netlister
  Makes binary netlist basing on schematic symbols, Via Model, Model builder.
SimAPI
  Runs simulator of choice (HyperSim, ADSM, HSPISE) for a given binary netlist
EZWave
  WDB Server stores and handles waveforms for all time domain simulations

## Slide 6: Crosstalk and SSN effects
Hyperlynx supports automatic aggressor selection using
  Trace coupling thresholds: geometrical or electrical
  IBIS package coupling in dB
  Multiboard connector coupling in dB
  S-parameter coupling in dB: 3d areas in BS, blackbox in LS
  Power bus coupling for power-aware IBIS models
Manual nets selection by net list, net name mask(s) or RMB picks
  Simulation for all coupling effects above and PDN coupling for power-aware simulations
Use Manage Assigned model to check and update IBIS model selectors, active drivers, stimulus.

## Slide 7: SI Coupling Settings

## Slide 8: Multiple nets selection in BoardSim

## Slide 9: Nets selection in LineSim
Most important for DDR batch performance
Look and feel as in BoardSim.
  Manual, by net name(s) or RMB for selected symbols.
  Automatic for batch analysis – net by net.
  Includes aggressors basing on coupling s-parameter coupling thresholds (in dB)
Unselected black box ports get terminated as defined in touchstone model

## Slide 10: Summary

## Slide 11: 3D models - 3D Area Manager
3D area manager automatically creates areas around via and pins using HLDRC script

## Slide 12: 3D areas are solved in HLAS and exported to LS

## Slide 13: 3D models - Hybrid modeling
Use PDN & Channel Export Wizard to choose signal and power nets and solve it in HLAS.
Import solved s-parameter model(s) into BoardSim. It gets associated with signal nets using port information from s-parameter header.
Now all SI simulations use this 3D model instead of 2D whenever net is involved in simulation. VX.2.12 supports mixes 2d and 3d models in one simulation (of cause without EM coupling between 2d and 3d sections)
Aggressors selected basing s-parameter coupling

## Slide 14: Summary

## Slide 15: Summary

## Slide 17: Interactive SI simulations
Two flows: Oscilloscope and EZwave
  Traditionally, HL customers prefer Oscilloscope.
  EZwave is more complex but powerful. It supports many views with annotations, includes waveform calculator, handles huge waveforms.
    Though all these features are overkill if all you do is comparing RX waveforms for two consecutive simulations.
EZWave with measurements
  Performs Timing/SI/Crosstalk measurements for selected signal. Works in BoardSim and LineSim.
  Essentially, it’s ancestor of General Batch
Interactive DDR5 simulation
  Run complex DDR5 data lane simulation interactively to prepare, assess and debug batch ddr5 simulations

## Slide 18: SI batch analysis
General Batch Wizard
  For low data rate signals
Pulse Respond Wizard
  Quick assess channel’s quality from RX pulse response basing o ISI/crosstalk metrics. Simple setup, no models.
DDRx Wizard
  Setup and analyze DDRx memory interface
  Inside it runs multibit SI simulations for clock, address, strobe and data lines
SerDes Wizard
  Check differential channel(s) for compliance with serial link protocols: PCIE, USB,
  Includes functions of deprecated FastEye Wizard

## Slide 19: SI concerns for different data rate

## Slide 20: How to assess signal quality
Traditional SI measurements based on Vinh, Vinl switching thresholds.
  Usually applied for a couple of pulses, originally just for the rising/falling edge. Used mostly to check slow switching signals with no jitter, no ISI, etc.
  Min/Max delay
  Static overshoot, Dynamic overshoot, Ringback, Monotonicity
  Crosstalk
  Constraints are defined per Net or Net Class in BoardSim.
Eye diagram / eye mask – for a long series of bits
  Includes jitter and ISI effects

## Slide 21: Traditional SI measurements

## Slide 22: General Batch Wizard
Runs

## Slide 23: General Batch Wizard
Quick Analysis
SI Analysis (timing, SI, crosstalk)
EMC Analysis

## Slide 24: General Batch Wizard: results
Quick Analysis SI measurements

## Slide 25: Pulse Response Wizard
Based on Intel’s Channel Checking Tool (CCT)

## Slide 26: Pulse Response Wizard
GUI is very similar to General Batch Wizard.
  You select nets, driver/receivers, termination (per net class) and hit Run.

## Slide 27: Summary

## Slide 28: Pulse Response Wizard

## Slide 29: Summary

## Slide 30: DDRx data rate

## Slide 31: DDR routing topology

## Slide 32: Summary

## Slide 33: Summary
The end

## Slide 34: Analyzing Serial Channels for Protocol Compliance
Dozens of specs, hundreds of pages (each)
    Who has time to read them?
Differing analytical methods and Pass/Fail criteria:
    Time-domain (eye masks)
    Frequency-domain (frequency masks)
    Channel Operating Margin (COM metric)
    JEDEC Channel Operating Margin (JCOM metric)

## Slide 35: DDR5 simulations
USE IBIS-AMI models with DFE equalization for single-ended DDR data lines
Flows:
  Statistical AMI
  Time Domain AMI
  Advanced DDRx AMI.
    Aka 4-steps flow, requires 2 long time domain simulations
    More accurate, accounts for non-linear TX effects.
Really long simulations, usually more than 25K bits. Marketing expectation 1M bits.

## Slide 36: Interactive DDR5 simulation

## Slide 37: Summary

## Slide 38: Via model in HyperLynx SI/PI
Via model in HL SI/PI is not power aware. But it attempts to estimate the effect of the return current transition between the planes.
If we inspect the via equivalent circuit in HL SI/PI we can find the large inductance between the plane layers. This one estimates the return current transition effect.
This inductance estimates the effect of the return current transition between the planes

## Slide 39: Empty page

## Slide 40: Summary